## Slide 1: HEART RATE MEASUREMENT FROM FACIAL VIDEO
GUIDE:
DR.L. SAIRAMESH
Bhuvaneshwari P,
2019202008,
MCA-Regular.

## Slide 2: OVERALL ARCHITECTURE

## Slide 3: LIST OF MODULES
Video capture
Facial landmarks detection and tracking
ROI detection and tracking
Frame conversion
Eulerian video magnification
Image processing
Signal processing
Data plotting
Heart Rate Measurement

## Slide 4: SHAPE PREDICTOR FACIAL LANDMARKS
Facial landmarks are used to localize and represent salient regions of the face, such as:
    Eyes
    Eyebrows
    Nose
    Mouth
    Jawline
Facial landmarks have been successfully applied to face alignment, head pose estimation, face swapping, blink detection and much more.

## Slide 5: EULERIAN VIDEO MAGNIFICATION
COLOR MAGNIFICATION
GAUSSIAN PYRAMID
MOTION MAGNIFICATION
LAPLACIAN PYRAMID

## Slide 6: FAST FOURIER TRANSFORM
The component signals were fast Fourier transformed.
An FFT converts the component signals into an estimation of power spectra (squared magnitude) .
A high peak in power at a certain frequency means that the component was made up mostly of a sine-wave at that specific frequency.
This frequency is in most cases a reflection of the detected heart rate.

## Slide 7: MODULES IMPLEMENTATION (80%)
Camera: Get the live video from user and covert the video into frames.
Input: captured video, output: frames.
Image Processing: Whole-frame image processing components & helper methods
RGB split: Extract the red, green, and blue channels from an (n,m,3) shaped array representing a single image frame with RGB color coding.
RGB mux: Take three (m,n) matrices of equal size and combine them into a single RGB-coded color frame.
CV wrap: Generic wrapper to take the simpler functions from the cv2 or SciPy image libraries to generate connectable openMDAO components for image processing.

## Slide 8: _
Gray scale: Turn (m,n,3) shaped RGB image frame to a (m,n) frame. Discards color information to produce simple image matrix.
Equalise contrast: Automatic contrast correction for grayscale images.
Face Detection: Defect the face with haar cascade Algorithm.
ROI Detection: Defect the sub region in the face.
Signal Analysis: signal Frequency analysis with Fast Fourier Transform(FFT)
Data plotting: plot the obtained bpm in power spectral density and raw signal.
BPM plot: the estimated heart rate plotted in frame.

## Slide 9: SIGNAL PROCESSING
Process within data buffer size
Calculate true fps for interpolation
Spectral leakage
FFT
Pruned FFT
Heart rate estimation

## Slide 10: OUTPUT SCREENSHOT

## Slide 11: UNIT TESTING WITH TEST CASES FOR EACH MODULE

## Slide 12: -

## Slide 13: _

## Slide 14: _

## Slide 15: _